UNIVERSITY OF NAIROBI

SCHOOL OF ENGINEERING

DEPARTMENT OF ENVIRONMENTAL AND BIOSYSTEMS ENGINEERING

PROJECT DESIGN REPORT

TITLE: DESIGN OF AN UNDERGROUND RAINWATER HARVESTING AND STORAGE SYSTEM IN KAJIADO WEST CONSTITUENCY FOR A FARM IN OLOOSEOS AREA.

NAME: ALOE FLAWIN GULENYWA.

REGISTRATION NUMBER: F21/37433/2016.

SUPERVISOR: DR. J.P.O. OBIERO.

COURSE COORDINATOR: ENG. DANIEL A. MUTULI

This Project Design Report Is Submitted In Partial Fulfillment of the Requirements of the Degree of Bachelor of Science in Biosystems Engineering Of The University Of Nairobi.

DECLARATION

I ALOE FLAWIN GULENYWA, of Registration Number F21/37433/2016, do hereby declare that the project entitled “Design Of An Underground Rainwater Harvesting

And Storage System In Kajiado West Constituency for a farm in Olooseos Area” submitted to The Department of Environmental and Biosystems Engineering, University of Nairobi, is a record of an original work done by me under the guidance of my Supervisor Dr. J.P.O. Obiero and Course coordinator Eng. Daniel A. Mutuli I further declare that the work reported in this project has not been submitted and will not be submitted, either in whole or in part for a degree or any other academic award in any other Institution or University.

Signature ……………………………….. Date ……………..…………………

ALOE FLAWIN GULENYWA.

REG. NO.: F21/37433/2016.

Approval:

This project has been submitted for examination with my approval as the University

Supervisor.

Signature………………………………. Date ………………………………….

DR. J.P.O. OBIERO

i

DEDICATION

I dedicate this project to my family, my parents, who have always been a source of motivation throughout my life, especially my educational life. My siblings who have pushed me towards my achieving my goals in life, Thank you for believing in me. To my friends, “we did it joe”- Kamala Harris. To my Honorable Lectures thank you for the effort, you put in to make this happen.

ii

ACKNOWLEDGEMENT

At First, I praise God Almighty who gave me the strength and the resources needed for this course and the accomplishment of my project. I thank Him for the opportunity, capability, energy, spirit, and patience to complete this project.

I would like to express my deepest appreciation to all those who supported me through this project. Special gratitude to my Supervisor Dr. J.P.O Obiero for his sacrifice and dedication.

To my course coordinator Eng. Daniel A. Mutuli for the encouraging word, guidance, and motivation through this project.

Lastly, I would like to acknowledge and appreciate the University of Nairobi Department of Environmental and Biosystems Engineering headed by Dr. D.O. Mbuge and my classmates who were a source of great value, comfort during my university life. I wish to thank them for the consultations and the support they offered me.

iii

ABSTRACT

Water is an important resource to human survival and with the increasing population and climate change; it has become a scarce commodity. The available water sources such as rivers are inadequate to fulfill water demand due to the low amounts of rainfall experienced in recent years. The main sources of water are surface water, groundwater, and rainwater.

The prolonged natural disasters such as droughts have contributed highly to the inadequacy of water, especially in arid and semi-arid areas. This in return has affected agriculture as a body, which has led to the scarcity of food for the ever-growing population. To try and minimize this, most people in the world have opted for Rainwater harvesting as a means to maximize the available water.

The main objective of the study is to Design an Underground Rainwater Harvesting and Storage System for a farm in Olooseos Area, a semi-arid area, and this project asserts that the only solution to maximize rainwater is to come up with a system that will harvest and store surface-water that will be useful for agricultural purposes during the dry season.

Suitable areas for the design of the underground water tanks had to be identified and selected both physically and through contour generation. A conveyance network suitable for the community in the area was designed with the idea of flash flooding as a challenge. Rainfall data over the past years were acquired and analyzed to keenly understand the rainfall patterns. More data was acquired through questionnaires and the daily water demand was useful in the determination of the tank capacity.

The developed system satisfies the social requirements and can be implemented in rural areas by considering almost all the technical aspects.

iv

TABLE OF CONTENTS

i

DECLARATION	i

DEDICATION	ii

ACKNOWLEDGEMENT	iii

ABSTRACT	iv

TABLE OF CONTENTS	v

LIST OF FIGURES	viii

LIST OF TABLES	x

ABBREVIATIONS	xi

INTRODUCTION:	1

1.1	BACKGROUND:	1

1.2 PROBLEM STATEMENT AND JUSTIFICATION:	2

1.4 SITE DESCRIPTION:	5

1.5 OBJECTIVES:	12

1.5.1 BROAD OBJECTIVE:	12

1.5.2 SPECIFIC OBJECTIVES:	12

1.6 PROJECT SCOPE	12

2.0	LITERATURE REVIEW:	13

2.1 Rainwater Harvesting	13

2.2 Components of a Rainwater Harvesting System:	13

2.3 Storm Water Harvesting.	15

2.4 Storage of Harvested Water:	16

2.5 Water Demand Management (WDM):	18

2.6 Water Demand per Capita per Day:	18

2.6 Siltation:	18

2.6 Flash Flooding:	18

2.7 Merits of underground RWHS over other RWHS	20

2.8 Demerits of underground RWHS to other RWHS	21

2.9 Uses of harvested rainwater:	22

2.9.1Uses:	22

2.9.2 Benefits of Rainwater Harvesting	23

2.9.3 The disadvantage of Rainwater Harvesting	23

3.0 THEORETICAL FRAMEWORK:	24

v

3.1 Determining Harvested water.	24

3.2 Dry Season Storage Method:	25

3.3 Storage Capacity:	25

3.4 Storage Tank Capacity/Volume.	25

3.5 Rainwater harvesting potential:	26

3.6 Runoff Coefficient:	27

3.7 Mass Curve Analysis:	28

3.8 Conveying Network Design	28

3.9 DIMENSIONING OF THE CONVEYANCE SYSTEM.	29

4.0 METHODOLOGY:	30

4.1Description of the Study Area:	30

4.2. Design Requirements:	31

4.3 Data Collection:	31

4.4 Data analysis:	33

4.5 Required software:	33

4.6 Strategic and Main Project Activities:	34

4.10 Determination of conveyance network:	35

4.11 Controlling Flash Flooding:	39

4.12 Controlling Siltation:	39

5.0 PRELIMINARY SKETCH	40

6.0 RESULTS AND DISCUSSION:	41

6.1 Area of Study:	41

6.2 Climate	41

6.3 Determination of Water Demand	42

6.4 Water Demand per Capita per Day:	43

6.5 How RW is used by the people in Olooseos area:	44

6.5 CLIMATIC DATA	45

6.6 PRECIPITATION DATA FROM 01/01/2021 THROUGH 05/03/2021	54

6.7 TANK CAPACITY:	57

6.8 QUESTIONNAIRES	58

7.0 CONCLUSION AND RECOMMENDATIONS	59

7.1 CONCLUSION	59

7.2 RECOMMENDATIONS	60

9.0 BILL OF QUANTITIES	61

10.0 REFERENCES:	63

11.0 APPENDICES	65

vi

APPENDIX A: AUTOCAD DRAWINGS	65

Appendix A-1a Underground Tank Drawing	65

APPENDIX B: STUDY AREA OLOSEOOSE AREA	66

Appendix B-1 Ngong hills	66

Appendix B-2 Ngong Hills view from my study area	67

Appendix B-3 a, b, c, d Dried River Bed	68

Appendix B-4 Olooseos Road	70

Appendix B-5 a,b Rocks found on the sides of the road	71

Appendix B-6 a, b Steep Slope in Olooseos area	72

Appendix B-7 a, b Grazing Area	73

Appendix 8 a, b, c dried Up River bed.	74

Appendix 9 a, b Soil type	75

Appendix 10 a, b, c, d Olooseos dam	77

Appendix 11 a, b, c, d, e, f vegetation near Olooseos dam	79

Appendix 12 a, b, c, storage facilities from several households in Olooseos area	82

Appendix 12 d, a greenhouse in olooseos area	83

Appendix 13 Vegetation during the April – May 2021 rainy season	84

Appendix 14 Questionnaires from three households in Olooseos area	90

vii

LIST OF FIGURES

Figure 1: Kenyan Map.	6

Figure 2 Kajiado County	6

Figure 3: Kajiado County.	7

Figure 4: Kiserian Town.	7

Figure 5: Ngong Town.	8

Figure 6: Corner Baridi Area (Olooseos area) Kajiado West Constituency.	8

Figure 7: Kiserian Climate	9

Figure 8: Average Monthly Temperatures in Kajiado	9

Figure 9: Daylight hours/ Sunshine Hours-Kajiado, Kenya.	10

Figure 10: Humidity – Kajiado, Kenya.	10

Figure 11: Rainfall-Kajiado, Kenya	11

Figure 12: Sump type for the first diverter.	14

Figure 13: Components of Rainwater Harvesting (RWHS)	14

Figure 14: Underground Storage Tank.	15

Figure 15: Stormwater Harvesting	15

Figure 16: Stormwater Management	16

Figure 17:Shows a representation of a 3 chambered septic tank (Jason 2019).	17

Figure 18:showing the impact of flash floods in Kajiado, Kiserian River, and Road

Covered with floods (Agency 2020).	19

Figure 19:showing the impact of flash floods near Kiserian River, Road with no rail

(KNU 2018).	19

Figure 20:Showing the impact of flash floods near Kiserian River, Road after

Construction of rail (Press and NEWS 2019).	20

Figure 21: Personal Sketch drawing of the three-chambered underground tank.	21

Figure 22: Gabion for stream control (Aird 2017).	22

Figure 23: Kajiado County- the percentage of Households with improved and

unimproved sources of water by ward	30

Figure 24: Concrete drainage.	37

Figure 25: open concrete ditch	37

Figure 26:Landscaping to deal with stormwater	38

Figure 27: showing a simple lined channel in the University of Nairobi Kabete Campus.

38

Figure 28: showing a simple unlined channel in Kajiado Olooseos area.	39

Figure 29: Kiserian Average Temperature.	41

viii

Figure 30: Kiserian Weather by Month/ Weather Average, variations in the precipitation

between the driest and wettest months is 169 mm/7 inch. The variation of temperature

throughout the year is 3.8 degrees Celsius or 38.8 Fahrenheit	42

Figure 31. Water Demand per Capita per Day (Mohanty 2012)	43

Figure 32: Graphical representation of Precipitation From 2010 – 2019 (Olooseos

area)(NASA 2021).	51

Figure 33: Graphical representation of Relative Humidity From 2010 – 2019 (Olooseos

area)(NASA 2021).	51

Figure 34: Graphical representation of Temperature at 2 Meters From 2010 – 2019

(Olooseos area)(NASA 2021).	52

Figure 35: Graphical representation of Maximum Temperature at 2 Meters From 2010 –

2019 (Olooseos area)(NASA 2021).	52

Figure 36: Graphical representation of Minimum Temperature at 2 Meters From 2010 –

2019 (Olooseos area)(NASA 2021).	53

Figure 37: Graphical representation of Temperature Range at 2 Meters From 2010 – 2019

(Olooseos area)(NASA 2021).	53

Figure 38: Graphical representation of Wind Speed at 10 Meters From 2010 – 2019

(Olooseos area)(NASA 2021).	54

Figure 39: Graphical representation of Precipitation From 1ST January 2021 – 31ST May

2021 (Olooseos area)(NASA 2021).	56

Figure 40: Graphical representation of Precipitation From 1ST January 2021 – 31ST May

2021 (Olooseos area)(NASA 2021).	56

ix

LIST OF TABLES

Table 1: Runoff Coefficients	28

Table 2. Rainfall pattern and analysis in Kajiado west for the past 10 years (NASA 2021).

45

Table 3. Precipitation Data From 01/01/2021 Through 05/03/2021	54

Table 4. Summary Bill of Quantities	61

x

ABBREVIATIONS

RWHS – Rainwater Harvesting and Storage System RWH – Rainwater Harvesting

RW- Rainwater

KSH. – Kenya Shillings

PRECTOT – Precipitation

RH2M- Relative Humidity at 2 Meters

T2M Range – Temperature range at 2 Meters

T2M MAX- Maximum Temperature at 2 Meters

T2M MIN- Minimum Temperature at 2 Meters

T2M- Temperature at 2 meters

WDM - Water Demand Management

WS10M- Wind Speed at 10 meters

xi

INTRODUCTION:

1.1 BACKGROUND:

Water scarcity in Kenya has been a challenge for decades, as only a small percentage of the country’s land is optimal for agriculture, and a year-round climate is predominantly arid. Recent natural disasters such as drought and floods have also contributed to the inadequacy of water in the country. Kenya’s natural water resources also do not provide an equitable delivery of water to the various regions of the country and the country ’s water basins do not reach an equitable area of the country. This has led to most parts of the country having a challenge of water scarcity for human consumption and to even practice agriculture (Snyder 2006).

Kenya is a dry country with about 80 percent of the country being arid and semi-arid. The average annual rainfall in Kenya is 630mm with a variation from less than 200mm in Northern Kenya to over 1,800 on the slopes of Mt. Kenya.

Kenya’s economy depends highly on agriculture, with agriculture contributing about one-third of the country’s income. The high promising agricultural land amounts to only 17 percent which sustains 75 percent of the population (Marshall 2011).

Agriculture highly depends on water for it is the largest user of water globally. The water of appropriate quality and quantity is essential for the production of crops, livestock, and fisheries, as well as the processing and preparation of these foods and products.

Water is the lifeblood of the ecosystem, including forests, lakes, and wetlands on which the food and nutritional security of present and future generations depend. Climate change has had an impact on agriculture by increasing water demand, reducing water availability in most areas, and limiting crop productivity (LOSS 2019).

Having the means to harvest and store rainwater to improve agriculture in arid and semi-arid areas will be of great significance to the fast-growing population.

In search of sustainable solutions to water scarcity, Rainwater Harvesting (RWH) has been identified as a practical option to help control water shortage in arid and semi-arid areas of the Country. This is despite its main challenge of storage cost and space (Nega and Kimeu 2002).

1