UNIVERSITY OF NAIROBI

SCHOOL OF ENGINEERING

DEPARTMENT OF ENVIRONMENTAL AND BIOSYSTEMS

ENGINEERING

FEB 540: DESIGN PROJECT

DESIGN OF A CULTURED ALGAE BIOFUEL GENERATION SYSTEM FROM INORGANIC WASTE FOR RUIRU SUB-COUNTY

NAME:

KANYARI ANTONY MBUGUA

REGISTRATION NUMBER:

F21/4323/2017

SUPERVISOR:

DR DUNCAN ONYANGO MBUGE

CO-SUPERVISOR:

MS MARIANA WANZA

COURSE COORDINATOR:

ENG. MUTULI DANIEL A.

A report submitted in partial fulfillment for the Degree of Biosystems Engineering in the Department of Environmental and Biosystems Engineering at the University of Nairobi

DECLARATION

I declare that this project is my work and has not been submitted for the conferment of a degree in any other University

Date:

Sign

11/06/2021

MBUGUA K. ANTONY

This project has been submitted to me for examination with approval as a University supervisor.

Date:

Sign

11/06/2021

MS MARIANA WANZA

i

DEDICATION

This project is dedicated to my deceased grandmother Mrs. Margaret Njeri, my parents Mr. John M. Kanyari, and Mrs. Joyce Wairimu who have been an encouragement to me throughout my stay at the University of Nairobi.

ii

ACKNOWLEDGEMENT

I wish to express my sincere gratitude to my project supervisor Ms. Mariana Wanza for her invaluable help, guidance, and support throughout the project design period.

I would also like to appreciate, the Kenya Bureau of Statistics and SuperPro designer model for assistance in data acquisition for the project.

My sincere gratitude goes to my classmates and the Biosystems Engineering fraternity for their encouragement and contribution towards the project design.

I am greatly indebted to my family for their constant encouragement and support.

iii

ABSTRACT

With fluctuating prices of oil in the market and the poor inorganic waste disposal sites in Ruiru sub-county, it has necessitated the design of a system that is able to utilize this waste to produce a biofuel that will meet the demand required by the area.

This design project entails an incineration system that will be able to convert total inorganic waste into desired carbon dioxide which will be synthesized by algae for photosynthesis. The project also entails the design of algae pond raceways which will produce enough algae to be synthesized to biofuel.

The design project does economic analysis for conversion of algae into algae oil and conversion of algae oil to biofuel and found to be beneficial compared to when the project isn’t there. Finally, the design drawings for fabrication are present in the appendices and the relevant data used in the project.

iv

LIST OF ABBREVIATIONS

NEMA- National Environment and Management Authority

NSWMB- National Sustainable Waste Management Bill

KPHC- Kenya Population and Housing Census

M3 – meter cubic volume.

MSW- Municipal Solid Waste

FB- Fluidized Bed

UK- United Kingdom

PBRs – Photobioreactors

LEDs- Light Emitting Diodes

To = total waste generated

Tp = total population

Av= average per capita waste generated

Ti = total inorganic waste

Iw =% of inorganic waste

Vo= volume of combustion chamber

Mp= mass of plastic in kg

Dpl= density of plastics in kg/m3

Vo = volume of algae pond not occupied by water Vt = total volume

Vw = working volume

Dp = depth of algae pond

Lp = length of pond

Ds =diameter of semicircle

Aa = area occupied by arc

Do = depth of smaller diameter of arc

v

D1 = large diameter of arc

Pn = number of plates

Ac = total angle of a circle

Ap = angle between each plate

Lpl = length of plate

Ls = length of shaft in pond

Sp = spacing in plates

Wp = width of plate

Aw= assumed percentage of width

Ac = area of cut plate

Tg = total gallons of oil consumed in Ruiru

Go = gallons per capita per year

Tw = total weight in kg of algae

Cf1 = conversion factor one

Tf = total weight of algae fed into the system

Wf = weight of algae fed into system

Wr = weight of algae required by system

Ta = total area of land required by project in km2 Cf2 = conversion factor 2

Ah = algae production per hectare

Np = number of ponds required by project

Pp = superPro designer given number of ponds

Tp = total hectare of land occupied by superPro designer ponds Sf1= scaling factor one

Ng = number of ponds required by project

Sf2 = scaling factor two

vi

Pb = project biodiesel required per year

Mb = model biodiesel production per year

Bv = biofuel revenue

Cf3 = conversion factor 3 in US$

Tr = total protein required

Tm = total protein produced by model

Tgr= total glycerol required

Tgm = total glycerol required by model

TC = total capital invested

NR = net revenue

vii

| DECLARATION....................................................................................................................... | i |
| --- | --- |
| DEDICATION.......................................................................................................................... | ii |
| ACKNOWLEDGEMENT ...................................................................................................... | iii |
| ABSTRACT | ............................................................................................................................. | iv |
| LIST OF ABBREVIATIONS ................................................................................................. | v |
| LIST OF FIGURES ............................................................................................................... | xii |
| LIST OF TABLE .................................................................................................................. | xiii |
| 1 | INTRODUCTION............................................................................................................ | 1 |
|  | 1.1 | Background ................................................................................................................. | 1 |
|  | 1.2 | Problem Statement ...................................................................................................... | 1 |
|  | 1.3 | Justification ................................................................................................................. | 2 |
|  | 1.4 | Statement of scope ...................................................................................................... | 2 |
|  | 1.5 | Site Analysis and Inventory ........................................................................................ | 3 |
|  | 1.6 | Overall Objective ........................................................................................................ | 4 |
|  | 1.6.1 | Specific Objectives .............................................................................................. | 4 |
| 2 | LITERATURE REVIEW ............................................................................................... | 5 |
|  | 2.1 | Algae oil ...................................................................................................................... | 5 |
|  | 2.1.1 | Algae Pond Section .............................................................................................. | 5 |
|  | 2.1.2 | Algae Harvesting Section .................................................................................... | 6 |
|  | 2.1.3 | Hexane Extraction Section ................................................................................... | 7 |
|  | 2.1.4 | Degumming Section............................................................................................. | 7 |
|  | 2.1.5 | Anaerobic digestion ............................................................................................. | 8 |
|  | 2.1.6 | Cogeneration section ............................................................................................ | 8 |
|  | 2.2 | Biofuel ....................................................................................................................... | 10 |
|  | 2.2.1 | Reaction Section ................................................................................................ | 10 |
|  | 2.2.2 | Biofuel Refining Section.................................................................................... | 11 |
|  |  |  |  | viii |

|  | 2.2.3 | Glycerol Purification Section ............................................................................. | 11 |
| --- | --- | --- | --- |
| 3 | Theoretical framework .................................................................................................. | 13 |
| 3.1Determination of algae pond raceway parameters .................................................... | 13 |
|  | 3.1.1 | Determination of volume of water not occupied by water ................................ | 13 |
|  | 3.1.2 | Determination of surface area of algae pond dimensions .................................. | 13 |
|  | 3.1.3 | Determination of length of raceway pond ......................................................... | 13 |
|  | 3.1.4 | Determination of small diameter of arc ............................................................. | 13 |
| 3.2Determination of raceway paddle parameters ........................................................... | 14 |
|  | 3.2.1 | Determination of number of plates .................................................................... | 14 |
|  | 3.2.2 | Determination of dimensions of plate ................................................................ | 14 |
|  | 3.2.3 | Determination of width of plate ......................................................................... | 14 |
|  | 3.2.4 | Area of cut section of plate of plate ................................................................... | 14 |
| 3.3Economic analysis of project .................................................................................... | 15 |
|  | 3.3.1 | Total gallons consumed in Ruiru ....................................................................... | 15 |
|  | 3.3.2 | Total weight in kg of algae ................................................................................ | 15 |
|  | 3.3.3 | Total weight of algae fed into the system .......................................................... | 15 |
|  | 3.3.4 | Total area of land required by project ................................................................ | 15 |
|  | 3.3.5 | Number of ponds required by project ................................................................ | 16 |
|  | 3.3.6 | Scaling factor 1 .................................................................................................. | 16 |
|  | 3.3.7 | Scaling factor 2 .................................................................................................. | 16 |
|  | 3.3.8 | Biofuel revenue .................................................................................................. | 16 |
|  | 3.3.9 | Total protein revenue ......................................................................................... | 16 |
|  | 3.3.10 | Total glycerol required ....................................................................................... | 17 |
|  | 3.3.11 | Return period ..................................................................................................... | 17 |
| 4 | MATERIALS AND METHODS .................................................................................. | 18 |
| 4.1Comparative Analysis to Show Algae as Best Feed Stock ....................................... | 18 |
|  |  | ix |  |

| 4.1.1 | Comparative analysis for the best microalgae strain ......................................... | 18 |
| --- | --- | --- |
| 4.1.2 | Comparative Analysis for Best Algae Culturing Technique ............................. | 18 |
| 4.2 | Design parameters for the system. ............................................................................ | 18 |
| 4.2.1 | Incinerator design parameters ............................................................................ | 18 |
| 4.2.2 | Algae Pond Design Parameters .......................................................................... | 19 |
| 4.2.3 | Raceway Paddle Design Parameters .................................................................. | 19 |
| 5 | RESULTS AND ANALYSIS ....................................................................................... | 20 |
| 5.1 | Comparison table for various biofuel feedstock ....................................................... | 20 |
| 5.2 | A table showing comparison of methods of culturing algae ..................................... | 21 |
| 5.3 | Design parameters ..................................................................................................... | 22 |
| 5.3.1 | Incinerator design parameters ............................................................................ | 22 |
| 5.3.2 | Algae Pond Design Parameters .......................................................................... | 24 |
| 5.3.3 | Raceway Paddle Design Parameters .................................................................. | 25 |
| 5.4 | Economic Analysis .................................................................................................... | 27 |
| 5.4.1 | Economic Analysis for Algae Oil ...................................................................... | 27 |
| 5.4.2 | Economic Analysis of Biofuel ........................................................................... | 33 |
| 5.4.3 | Total cost of the project ..................................................................................... | 39 |
| 5.4.4 | Revenue generated by project project ................................................................ | 40 |
| 5.4.5 | Income generated and return period of the project ............................................ | 41 |
| 6 | DISCUSSION ............................................................................................................... | 42 |
| 6.1 | Algae is the best feedstock ........................................................................................ | 42 |
| 6.2 | Design parameters ..................................................................................................... | 42 |
| 6.2.1 | Incinerator design parameters ............................................................................ | 42 |
| 6.2.2 | Algae pond ......................................................................................................... | 42 |
| 6.3 | Economic analysis ..................................................................................................... | 43 |
| 7 | CONCLUSION AND RECOMMENDATION ............................................................ | 44 |
|  |  | x |  |

|  | 7.1 | Conclusion ................................................................................................................. | 44 |
| --- | --- | --- | --- |
|  | 7.2 | Recommendation ....................................................................................................... | 44 |
|  | 8 | APPENDICES .............................................................................................................. | 45 |
|  | 8.1 | Appendix 1 ................................................................................................................ | 45 |
|  | 8.2 | Appendix 2 ................................................................................................................ | 46 |
|  | 8.3 | Appendix 3 ................................................................................................................ | 47 |
|  | 8.4 | Appendix 4 ................................................................................................................ | 48 |
|  | 8.5 | Appendix 5 ................................................................................................................ | 49 |
|  | 8.6 | Appendix 6 ................................................................................................................ | 50 |
|  | 8.7 | Appendix 7 ................................................................................................................ | 51 |
|  | 8.8 | Appendix 8 ................................................................................................................ | 52 |
|  | 8.9 | Appendix 9 ................................................................................................................ | 53 |
|  | 8.10 | Appendix 10 .......................................................................................................... | 54 |
|  | 8.11 | Appendix 11 .......................................................................................................... | 55 |
|  | 8.12 | Appendix 12 .......................................................................................................... | 56 |
|  | 8.13 | Appendix 13 .......................................................................................................... | 57 |
|  | 8.14 | Appendix 14 .......................................................................................................... | 58 |
| 9 | References ....................................................................................................................... | 59 |

xi

LIST OF FIGURES

Figure 1 Northlands site	3

Figure 2 optimal temperatures for algae	3

Figure 3 temperature variation for kiambu	3

Figure 4 sunlight in hours for kiambu	4

Figure 5 algae raceways	6

Figure 7 YIELD OF ALGAE AND OTHER BIODIESEL CROPS	20

Figure 8 CHART OF VARIOUS MICROALGAE STRAINS AND LIPID CONTENT IN

THEM	21

Figure 9 population	23

Figure 10 Annual Operating Cost Breakdown(%)	33

xii

LIST OF TABLE

Table 1 30% oil (L/wt) in algae biomass, ** 70% oil (L/wt) in algae biomass	20

Table 2 5.1.1	Comparison table for best microalgae strain for culturing	20

Table 3 5.2	A table showing comparison of methods of culturing algae	21

Table 4 5.4.1.3	Major Equipment Specification and Fob Cost	28

Table 5 5.4.1.4	Fixed Capital Estimate Summary	31

Table 6 5.4.1.3	Labor Cost - Process Summary	31

Table 7 5.4.1.3	Materials Cost - Process Summary	31

Table 8 1.1.1.1	Utilities Cost - Process Summary	32

Table 9 5.4.1.4	Annual Operating Cost - Process Summary	33

Table 10 5.4.1.3	Executive Summary	33

Table 11 5.4.2.2	Major Equipment Specification and Fob Cost	34

Table 12 5.4.2.2	Fixed Capital Estimate Summary	38

Table 13 5.4.2.2	Labor Cost - Process Summary	38

Table 14 5.4.2.2	Materials Cost - Process Summary	38

Table 15 5.4.2.2	Utilities Cost - Process Summary	38

Table 16 5.4.2.2	Annual Operating Cost - Process Summary	39

Table 17 Annual Operating Cost Breakdown (%)	39

Table 18 5.4.2.2	Executive Summary	39

Table 19 5.4.3.1	Total capital invested in the project	39

Table 20 5.4.3.1	Total operating cost for the project	40

Table 21 5.4.4.1	Total revenue produced by project	41

xiii

1	INTRODUCTION

1.1	Background

Manufacturing and food security is one of the pillars in the big four agenda(BETH KAMENE, 2021). Ruiru sub- county being the capital of Kiambu exhibits many industries. One major commodity running the manufacturing industry is oil since it has very many applications ranging from production of plastics and other products to running and cooling of various machinery.

Food security is the other pillar of the big four agenda(BETH KAMENE, 2021). Oil has significant inputs in the food security sector through agricultural mechanization. The country over the past few years has shown increased use of tractors and other fuel driven agricultural implements to increase food production.

Oil touches everyone, from beauty products, plastics, vehicles, to almost unlimited applications but the commodity is non-renewable and at a later date it will completely be scarce.