UNIVERSITY OF NAIROBI

DEPARTMENT OF BIOSYSTEMS ENGINEERING

FEB 540: ENGINEERING DESIGN PROJECT

PROJECT REPORT

DESIGN OF A RAINWATER HARVESTING SYSTEM FOR A HOUSEHOLD FOR DOMESTIC USE IN MAKIMENY VILLAGE, BOMET COUNTY

MAKERER DAISSY CHELANGAT

F21/2261/2017

SUPERVISOR: MR. STEPHEN CONRAD ONDIEKI

COURSE COORDINATOR: ENG. MUTULI DANIEL A.

A thesis submitted in partial fulfillment of the requirements in the award of a degree in Bachelor of Science in Biosystems Engineering in the University of Nairobi

June 6, 2021

DECLARATION

I declare that this thesis is my original work and has not been submitted for a degree in any other University.

Sign ………………………. MAKERER DAISSY CHELANGAT

Date ………………………

This thesis has been submitted for examination with my approval as university supervisor.

MR. STEPHEN CONRAD ONDIEKI Sign ……………………….

Date ………………………

This thesis has been submitted for examination with my approval as university coordinator. ENG. D. A. MUTULI

Sign ……………………….	Date ……………………….

i

DEDICATION

This work is dedicated to my family: my parents Mr. and Mrs. Makerer, my siblings Gaylord, Edwin and Sally and to all who supported me. May God bless you.

ii

ACKNOWLEDGEMENT

I thank God for his provision and protection through this project. Secondly, I would like to acknowledge the input and positive criticism that I got from my supervisor, Mr. Stephen C. Ondieki, in writing this project report. I wish to express my sincere and heartfelt gratitude to the entire academic staff of the University of Nairobi Department of Environmental and Biosystems Engineering for their contribution throughout my studies. I also extend my gratitude to my fellow students and friends of the University of Nairobi for their continuous support and encouragement in my studies. Special thanks to the family of Mr. Amos Koech for allowing me to pilot for them and for providing the necessary data that I required. I would also like to commend the Kenya Meteorological Department (KMD) for their support during the data collection process. I am forever indebted to my parents, who have always been of great support in every step of my academics.

To every group or person that I have not mentioned, kindly accept my appreciation and may God bless you.

iii

ABSTRACT

Kenya is evaluating the need for a policy on integrating rainwater harvesting systems when developing residential units in both urban and rural areas as part of its water sector reforms. This will have to be incorporated into the various bodies that are tasked with developing rural water supply systems. With increase in population in Bomet County, low-cost initiatives such as rainwater harvesting are a top priority for households facing the problem of access to water. This project therefore aims at designing a rainwater harvesting system for one of the households in Makimeny Village, Bomet County. The system was designed to meet the water requirements of the household, especially during the dry seasons. Data was collected from the Kenya Meteorological Department and from the household using a camera and a notebook. The findings from the design process indicated that the selected area of study receives a significant amount of rainfall annually and, therefore, meets the water demands of the household. From the household and rainfall data collected, harvestable water from the roof catchment and weekly water demand were obtained. Each component was sized to ensure optimum collection of rainwater. The findings from this design project will not only assist the selected household to easily access water but also shed some light on the need for extensive and accessible water sources in rural Kenya. This project also forms a basis for future water projects in the selected area of study, such as the design of a water supply system by gravity to address the issue of water accessibility.

iv

TABLE OF CONTENTS

CHAPTER ONE	1

INTRODUCTION	1

1.1 Background Information	1

1.2 Problem statement	2

1.3 Justification and significance of the project	3

1.4 Objectives	4

CHAPTER TWO	5

LITERATURE REVIEW	5

2.1 Introduction	5

2.2 Types of Rainwater Harvesting Systems	7

2.3 Components of a Rainwater Harvesting System	7

2.4 Theoretical Framework	11

2.5 Reasons for Rainwater Harvesting	13

2.6 Factors affecting Rainwater Harvesting	14

2.7 Conceptual Framework	15

2.8 Logical Framework	17

CHAPTER THREE	18

METHODOLOGY	18

3.0 Introduction	18

3.1 Rainfall characteristics	18

3.2 Rainfall data	19

3.3 Water Demand	19

3.4 Harvestable Water	20

3.5 Sizing of the system components	22

CHAPTER FOUR	28

SITE ANALYSIS	28

4.0 Location and Size	28

4.1 Water Sources and Access	29

4.2 Climate	30

4.3 Physical and Topographic Features	31

v

4.4 Water Resources	31

4.5 Socio-economic activities	32

4.6 Ecological Conditions	32

4.7 Water Management	32

CHAPTER FIVE	34

RESULTS AND DISCUSSION	34

5.1 Water demand	34

5.2 Rainfall data	35

5.3 Rooftop catchment area and perimeter	37

5.4 Rainwater Harvesting Potential	37

5.5 Determining tank capacity	38

5.6 Determining capacity of gutters and downpipes	42

5.8 Bill of Quantities	45

CHAPTER SIX	47

CONCLUSION AND RECOMMENDATIONS	47

5.0 Conclusion	47

5.1 Recommendations	47

References	49

7.0 APPENDICES	51

vi

LIST OF FIGURES

Figure 1; Elements of a Rainwater Harvesting System	11

Figure 2;The Conceptual Framework of Rooftop Rainwater Harvesting	16

Figure 3; Mass curve analysis for determining tank capacity	23

Figure 4:A map of Bomet County	28

Figure 5;Google earth capture of Makimeny Village	29

Figure 6;Community source of water in Makimeny village	30

Figure 7;Graph of annual rainfall for 30 years	36

Figure 8;Graph of average monthly rainfall	37

Figure 9;Mass curve from household data	39

Figure 10: Pond in Makimeny Village, Bomet County	51

Figure 11:Google earth capture of Makimeny Village, Bomet County	52

vii

LIST OF TABLES

Table 1:Water consumption rates based on intended use	20

Table 2:Type of roofs with their corresponding run-off coefficients	21

Table 3:Capacity of gutters and downpipes (adopted from Warwick University	27

Table 4: Water consumption rates based on intended use	34

Table 5:Rainfall data of Bomet County	36

Table 6:Rainfall intensity	43

Table 7;Capacity of gutters and downpipes (adopted from Warwick University DTU)	44

Table 8:Bill of Quantities for the rainwater harvesting system	46

viii

CHAPTER ONE

INTRODUCTION

1.1 Background Information

Easy access to quality water is a crucial measure of improved life in a community. With the continuous growth in the human population coupled with climate change and land-use activities, reliable water sources and supply systems continue to reduce. To sustain this growing population and accommodate these changes, the existing water supply systems should be more efficient, and rainwater harvesting systems ought to be adopted where other conventional systems lack, more specifically in rural Kenya. With a population of 50 million people, nearly half of Kenyans depend on poor - quality sources of water including ponds, shallow wells, and rivers. 48 percent of this population lack basic sanitation. These issues are particularly acute in rural Kenya, where residents are frequently unable to access piped water facilities. The average total coping costs for an inadequate or inaccessible water sources in rural Kenya are about $ 38 per month. In contrast, the average monthly water bill for a typical Nairobi household connected to a piped water system is just $4.46 for every month. This comparison illustrates the economic difficulties that rural households without piped connections face more often than those with piped water connections (Marshall S., 2011). There are, however, many places where usable pipe water connections do not provide a consistent, reliable flow of water. As a result, solutions such as drilling boreholes and developing rainwater harvesting systems are just as important in urban areas as they are in rural Kenya. Access to clean water is more important than ever for Kenyan households' health in order to safeguard themselves from the Covid-19 pandemic as well as other illnesses. This project design, if widely implemented, would enhance the quality of life in the chosen study area. It will also relieve women and children of the constant burden of water collection.